## Slide 1
Palm tree climber
By: Panimalar polytechnic college
Chennai-29

## Slide 2
Submitted by
Pydipati praneeth kumar (MECH)
T.Gokulakrishnan (ECE)
M.Mohanasundar (CE)
K.S. Rohinth khanna (MECH)

## Slide 3
Aim
The project presented here, focuses on designing a palm tree climbing tool that helps man to climb trees of a diameter range of 60-480mm easily with a green caterpillar action enhanced with a spring mechanism that further reduces a considerable amount of human effort

## Slide 4
Existing system

## Slide 5
Description of existing system
It consists of two frames Upper and lower
Lower frame used for foot staging and upper frame is used for comfortable seating and for a succeeding motion
Rideable by pulling up the device by legs like a green caterpillar action.

## Slide 6
Disadvantages of Existing system
Existing tool cannot be used for the following circumstances:
Trees with wet surfaces
Thorny trees
Trees with hard lumpy surfaces
Trees with a smooth bark
Only skilled person’s can handle the device

## Slide 7
Proposed System

## Slide 8
Description of the proposed system
Similar to the existing system we have frames Upper and lower
Lower frame used for footstaging and upper frame is used for comfortable seating and for a succeeding motion
Springs are attached between the two frames to perform an upward push and a downward pull
A pulley system is provided in the upper frame to easily deliver ice apples etc.. to the ground from the top of the tree

## Slide 9
Working
Sit firmly on the upper frame and place your feet in the lower frame’s foot staging area
Once a person sits, tension is applied to the spring making it to compress , when the user removes the tension by slightly raising himself the spring retracts automatically giving the person a boost and reducing his work
User then only needs to move the upper frame to proceed further, Climbing is made faster and easier because of retracting mechanism of the spring
If the person needs to get things down from the tree after he climbs up , a spiral pulley mechanism installed in the panel of the upper frame contains wires/ropes that is retractable once tension is applied it is pulled down once user removes the tension it retracts back to its original position

## Slide 10
3D View

## Slide 11
2D View
Left view
Front view
Top view

## Slide 12
Specification
Cost involved and estimation(Approx)
No | Name | Material | Qty/metre | Price
1 | Horn | Stainless steel | 10 m (3 ") | INR 1,500.00
2 | Lower frame | Stainless steel | 5m (8") | INR 1,250.00
3 | Safety rope | Rubberized Nylon | 1qt/3m | INR 300.00
4 | Upper frame | Stainless steel | 5m (8") | INR 1,250.00
5 | Metal-wire | Iron enclosed with rubber | 0.5m | INR 1,300.00
6 | Seat | Rubber |  | INR 1,750.00
7 | Retractable pulley | Motor spring |  | INR 1,500.00
8 | Fulcrum | Rubber with iron | 2qt | INR 200.00
9 | Coil spring | Music wire | 2qt | INR 5,000.00
10 | Limiting rope | Nylon | 2.5m | INR 250.00
 |  |  | Total material amount: | INR 14,300.00
 |  |  | Labour charge: | INR 3,000.00
 |  |  | Total amount : | INR 17,300.00
Estimated Market price: 9000 INR

## Slide 13
Pros & cons
Pros
Can be used on wet surfaces
Faster climbing
Pulley system for delivering objects from top of the tree
Safety rope with bowline knot
Rotatable around the trees
Unskilled person can handle
Cons
Cannot be used in thorny trees
Cannot be used with hard lumpy trees
Rotating is considerably slower

## Slide 14: FUTURE SCOPE
The device affords scope for modifications and further improvements. The weight of the equipment can be reduced by the use of alloys or composite material. It can be automated and can also include the climatic and cultivation details with the use of IOT. Also better safety accessories can be thought of and Included along with the equipment.

## Slide 15: CONCLUSION
The machine is built by following the natural phenomena present before us. Machine works on timely gripping and release of the tree by the two metal wire ropes locked to the moving frame. By this design, the structure is able to carry a load of 150kg and anyone can use it easily. At the beginning it is time consuming but with continuous use and practice it will reduced the time required for the Climbing. It is flexible to change the size of the equipment according to the requirement of the user. It has easy maintenance. The design and erection of this Equipment involved a great deal of effort to make the project successful and useful. We conclude the project on “PALM TREE CLIMBING” will be very useful in the field of agriculture.

## Slide 16: THANK YOU
PANIMALAR POLYTECHNIC COLLEGE
23,RAILWAY COLONY 2ND STREET,NELSON MANICKAM ROAD,CHENNAI-600029
Ph: 044-23741205,23743225
E-MAIL- info@pptc.ac.in
Website: www.pptc.ac.in